## Slide 1: Increasing Situational Awareness of River Flooding by applying a GIS Extent Mapping Approach
Jared Allen
NWS Austin/San Antonio
OK-SCAUG 06/24/15

## Slide 2: NWS Mission & Partnerships
Provide forecasts and warnings for protection of life and property.
Develop partnerships and relationships with City, County, State, and Federal agencies.
  Sharing data
  Sharing knowledge of local area
  Mitigating hazards before they happen
    NWS Norman & NWS Tulsa & NWS Amarillo (OK Panhandle)
Outlooks
Forecasts
Watches/Advisories
Warnings
Time
1-2 Weeks
1-7 days
6-36 hours
Hours - Minutes

## Slide 3: Record Setting Wet May
Flash Flood Fatalities 1996-2014
Flash Flood Fatalities 1996-2014

## Slide 4: Record Setting Wet May (& June)
Greg Carbin, SPC

## Slide 5: NWS Evolution of River Flooding Awareness
1) Tables to Text
2) Tables to
Graphics
Video Link

## Slide 6: Evolution of River Flooding Awareness Continued
Total of 127 gauge points completed since 2002 in response to inland flooding from Hurricane Floyd in 1999
3) Flood Extent and Inundation Mapping
4) Push Maps to EMs, Media, Web, Facebook, Twitter
Still several issues:
Money: $10,000 – $50,0008 per site
Plus Stringent NOAA/NWS Guidelines
Time: 3 Months to 2 Years8 per site
There has to be a better Effort vs. Cost way!
Only 2% of gauge sites mapped

## Slide 7: NWS/US Army Corps of Engineers Partnership
USACE Vicksburg, MS developed an in-house Flood Extent Simulation Model (FESM)
  Used with great success during Mississippi River Flood 2011
Met with USACE VKS about project idea for specific river sites
NWS Jackson developed an in depth protocol for ArcGIS & FESM integration (V1.7)
Built a local team, became regional (LMRFC), and then sub-national (Hydrologic Branch at WSH HQ) team

## Slide 8: River Flooding Extent Project Goals
Goal 1: To efficiently produce acceptably accurate flood extents for minor, moderate, major & record flood stages at and along river gauge sites (for a site specific distance) to aid both internal and external coordination and communication of the NWS with Federal, State, County and City officials, along with the general public.
Goal 2: To develop an intuitive internal & external dynamic web maps and information viewer displaying the flood stages.
Answer the questions of:
  What does moderate flood stage mean to me?
  What floods when the river reaches X feet?
  What areas of my city/county need to be monitored or possibly evacuated based on the river forecast?
  How much infrastructure is at risk if major flooding occurs?

## Slide 9: Project Methodology/Workflow
USACE FESM
Flood Extent Simulation Model
QC Filters in ArcMap
High Water
Marks Match
(E19s)
Minor
Gauge & Stream
Shapefiles created
DEM & LiDAR Area Selected
Phase 1 – Unedited Comparison
Phase 2 – Edited Comparison
FESM Shapefiles in ArcGIS
Inputs: Gauge & Stream Shapefiles
DEM, LiDAR Data
FEMA DFIRM
Agreement
Major
Record
Moderate
Minor
AHPS Shapefiles in ArcGIS
Major
Record
Moderate
Polygon to Raster
Reclassify
Raster Calculator
0 | 10
1 | 12
10 | 12
11 | 13
Minor
Major
Record
Moderate
Minor
Edited FESM Shapefiles in ArcGIS
Major
Record
Moderate
Minor
AHPS Shapefiles in ArcGIS
Major
Record
Moderate
Polygon to Raster
Reclassify
Raster Calculator
0 | 10
1 | 12
10 | 12
11 | 13
Unedited FESM Shapefiles
Place hypothetical gauge points upstream to downstream
Gauge 3 is an actual USGS/NWS River Gauge
Using the known height of the USGS/NWS gauge, use proportions to calculate the other hypothetical gauge heights
Need to account for vertical datum conversion as well (NGVD 1929 vs. NAVD 1988)
Polyline Stream segments going from downstream to upstream

## Slide 10: Project Methodology/Workflow
USACE FESM
Flood Extent Simulation Model
QC Filters in ArcMap
High Water
Marks Match
(E19s)
Minor
Gauge & Stream
Shapefiles created
DEM & LiDAR Area Selected
Phase 1 – Unedited Comparison
Phase 2 – Edited Comparison
FESM Shapefiles in ArcGIS
DEM, LiDAR Data Used
FEMA DFIRM
Agreement
Major
Record
Moderate
Minor
AHPS Shapefiles in ArcGIS
Major
Record
Moderate
Polygon to Raster
Reclassify
Raster Calculator
0 | 10
1 | 12
10 | 12
11 | 13
Minor
Major
Record
Moderate
Minor
Edited FESM Shapefiles in ArcGIS
Major
Record
Moderate
Minor
AHPS Shapefiles in ArcGIS
Major
Record
Moderate
Polygon to Raster
Reclassify
Raster Calculator
0 | 10
1 | 12
10 | 12
11 | 13
Unedited FESM Shapefiles
Alexandria, LA
Red River

## Slide 11: Sites Modeled and Statistics
Six river sites tested at various elevation data resolutions:
Spatial Statistical tests performed:
  Cohen’s Kappa Coefficient2,4
  Overall pixel classification accuracy6
    Computed for: Minor, Moderate, Major, and Record stages
River Site | LiDAR/DEM Resolution
Leaf River at Hattiesburg, MS | ~ 9 Feet (3 Meter) LiDAR
Susquehanna River at Binghamton, NY | ~ 6 Feet (2 Meter) LiDAR
Red River at Alexandria, LA | 20 Feet LiDAR
Susquehanna River at Harrisburg, PA | 30 Feet (10 meter) DEM
Kentucky River at Frankfort, KY | 5 Feet LiDAR
Onion Creek at Austin, TX | 30 Feet (10 Meter) DEM

## Slide 12: Cohen’s Kappa Coefficient
Assess inter-model reliability between two or more spatially observed/coded qualitative or categorical variables2.
 | Yes | No | Totals
Yes | 20 | 5 | 25
No | 10 | 15 | 25
Totals | 30 | 20 | 50
A
B
= Relative Observed Agreement
= Probability of Random Agreement
20 + 15 = 35 35/50 = 0.7
[(30/50) * (25/50)] + ([20/50) * (25/50)] = 0.5
= 0.40

## Slide 13
Minor
Moderate
Major
Record
Ƙ = 0.97
Ƙ = 0.82
Ƙ = 0.81
Ƙ = 0.82

## Slide 14: Results
Fig. 2
Unedited FESM Flood Extents had substantial to near perfect agreement.
  Record Stage performed the strongest on average across all sites (Austin, TX outlier)
  Moderate Flood Stage was weakest on average across all 6 sites (moderate agreement)
Using water impact location descriptions & FEMA DFIRM maps, edited flood extents (Fig. 2) had near perfect to substantial agreement.
  Excluding the minor and moderate stages for Frankfort, KY (High substantial agreement)
    Kappa could be raised further with local knowledge of Trumbo Bottom Area.
  Significant improvement for Alexandria, LA site in Bayou Maria Basin
  Moderate Flood Stage still lowest on average but above 0.8 (near perfect)
Flood Walls
Flood Walls
Backwater Flooding
Backwater Flooding
Flood Wall & Backwater Flooding
Flood Wall & Backwater Flooding
HEC-RAS Modeling Issues
HEC-RAS Modeling Issues
Fig. 1

## Slide 15: Flood Pixel Classification Accuracy
FCA = Pixels of FloodCorrect
(Pixels of FloodCorrect + Pixels of FloodOmission + Pixels of FloodCommission )
A series of flood classification accuracy graphs comparing unedited FESM Extents and edited FESM Extents against the accepted AHPS Extents were generated for:
- Minor - Moderate - Major - Record

## Slide 16
0.68
0.79
0.78
0.85
0.85
0.64
0.74
0.80

## Slide 17: Conclusions
FESM/ArcGIS Methodology deemed spatially accurate
  Effort vs. Cost Analysis
    70-98% FCA accurate and acceptable statistically
    Completed in a week or less (starting from scratch)
    With data in place & practice, can be as fast as 1-3 hours for raw flood area output & no QC
Mapping Accuracy & Kappa can be successfully increased through quality control measures:
  Set to match current Impact Statements – E19s
  FEMA DFIRM Data
  River Forecast Center Agreement
  Emergency Manager & Local Water Authority Agreement
Future Work
  Test more sites with current methodology
    Quantify QC improvements thru Classification and Kappa values
  Develop internal AGOL website for critical partner access.

## Slide 18: ArcGIS Online Integration
River Flooding Situational Awareness

## Slide 19: Online Flood Extent Viewer

## Slide 20: Critical for:
Key Decision Timelines
People and Resource Allocation
EOC Awareness & Service 1,7

## Slide 21: Thank You!
Cited Sources:
  Gall, M., Boruff, B., and Cutter, S. (2007). ”Assessing Flood Hazard Zones in the Absence of Digital Floodplain Maps: Comparison of Alternative Approaches.” Nat. Hazards Rev., 8(1), 1–12.
  Jeffrey D. Colby, Karen A. Mulcahy, and Yong Wang, 2000. Modeling flooding extent from Hurricane Floyd in the coastal plains of North Carolina. Global Environmental Change Part B: Environmental Hazards. 2(4), 157-168. http://dx.doi.org/10.1016/S1464-2867(01)00012-2.
  Michener, William & Houhoulis Paula. “Identification and Assessment of Natural Disturbances in Forested Ecosystems: The Role in GIS and Remote Sensing.” 1995 (http://www.ncgia.ucsb.edu/conf/SANTA_FE_CDROM/sf_papers/michener_william/michener.html)
  Short, Nicholas. Accuracy Assessment. (http://www.fas.org/irp/imint/docs/rst/Sect13/Sect13_3.html)
  Qi, S., Brown, D. G., Tian, Q., Jiang, L., Zhao, T., & Bergen, K. M. (2009). Inundation Extent and Flood Frequency Mapping Using LANDSAT Imagery and Digital Elevation Models. GIScience & Remote Sensing, 46(1), 101-127.
  Viera, Anthony, MD & Garrett, Joanne, PhD. “Understanding Interobserver Agreement: The Kappa Statistic.” Family Medicine. May 2005. (http://www1.cs.columbia.edu/~julia/courses/CS6998/Interrater_agreement.Kappa_statistic.pdf)
  Wilson, M. D., & Atkinson, P. M. (2005). The use of elevation data in flood inundation modelling: a comparison of ERS interferometric SAR and combined contour and differential GPS data. International Journal of River Basin Management, 3(1), 3-20.
  Weiger, Ben. NWS Flood Inundation Mapping Services, 2008. Bayou Vermillion River Conference. (http://www.srh.noaa.gov/media/lch/outreach/052808/6BenWeiger.pdf)
Jared Allen
Meteorologist/GIS – NWS Austin/San Antonio
Email: Jared.Allen@noaa.gov
NWS Norman Contact
Rick Smith – Warning Coordination Meteorologist
Email: Richard.Smith@noaa.gov

## Slide 22: To Find Cohen’s Kappa:

## Slide 23
Grid = 10
Grid = 1
Grid = 0
Grid = 12
Grid = 0 & 1
Grid = 10 & 12
AHPS
FESM
Mosaic to New Raster
Reclassify Raster
Reclassify Raster
Mosaic to New Raster

## Slide 24
Raster Calculator: Add the two Images together
Pixel Value | AHPS Flood | AHPS No Flood
FESM Flood | 13 | 11
FESM No Flood | 12 | 10
Four Number Combinations Possible:
10 – Both Agree No Flooding
11 – Flooding in AHPS but not in FESM
12 – No Flooding in AHPS but Flooding in FESM
13 – Both Agree Flooding